Mantis identifies a dynamic hydrothermal system on its Orphan property

Toronto, Ontario – July 16,2007- Mantis Mineral Corp (CNQ- MINT) is pleased to announce field crews have determined a dynamic hydrothermal system (the ‘Foisey Occurrence’) on its Orphan Gold Mine property. Historic grab samples of vein material from this occurrence have assayed up to 0.62 ounces gold per ton (21.3 grams per tonne), while channel samples ranged from 0.61 to 2.04 grams per tonne over widths of 3.0 to 5.8-meters. The system strikes at azimuth 135 to 160-degrees, similar to the “main vein” of the Orphan Mine, located 2,200-meters to the southeast. While these assays do not conform to National Instrument 43-101 they have been provided by the O.G.S. and are generally considered reliable according to local industry standards.

The Foisey Occurrence is characterized by; multi-generation mega-quartz veins and quartz stockworks veining, intense brecciation, incorporating centimeter-size intrusive inclusions, decimeter to meter-size metavolcanic xenoliths, strong alteration (potassic and silicic), 1-3% disseminated pyrite and occasional centimeter masses of chalcopyrite and minor molybdenite.

The occurrence was historically traced by intermittent trenching for 330-meters and varies in width from 7 to 10-meters. Mantis’ current claim fabric covers 266-meters of the known vein system. Its southeasterly extent remains open within the Mantis claim. Grab samples have been taken from the various showings and will be assayed shortly.

Commented Robin Ross, CEO, “Our initial exploration work on our 100% owned Orphan Gold Mine property continues to provide new and exciting developments.  We announced recently the discovery of a parallel vein  (the ‘north vein’) 100 meters to the north of the original vein which previously reported high grade assays above 11 oz pt gold. Now we have uncovered an entirely new system which may be linked to the original vein.  The next phase of work will include surface stripping, trenching, detailed channel sampling and tracing the systems  to determine whether they are indeed linked.”

Mantis Mineral Corp. is a Canadian exploration company with a portfolio of quality gold and base metal properties located in mining friendly northern Ontario.

Further information is available under the company’s profile at www.sedar.com.

Forward looking statements

This news release includes certain forward looking statements. Such forward looking statements contain risks and uncertainties. The results or events predicted in these forward looking statements may differ materially from actual results or events. Any forward looking statement speaks only as of the date of this news release and, as except as maybe required by applicable securities laws, the company disclaims any intent or obligation to update any forward looking statement, whether as a result of new information, future events, or results or otherwise.

The CNQ Exchange has not reviewed and does not accept responsibility for the adequacy of this release.

FOR FURTHER INFORMATION PLEASE CONTACT:

Mr. Robin Ross, Chairman & CEO 		 (416) 362-1800

rross@mantismineralcorp.com

NEWS RELEASE TRANSMITTED BY CNW Group